## Slide 1
Care of newborn under radiant warmer.
&
Care of baby under phototherapy.
Prepared by / Basem Rafat

## Slide 3
Radiant warmer:
is the device used to maintain the temperature of the baby and to prevent hypothermia.
Prepare a bed at least 30 minutes before the baby arrives in the nursery to ensure the baby is received in a warm, Comfortable environment.

## Slide 4
Procedure:
Getting ready:
1 – Wash hand.
2 – Wear the gloves.
3 – Prepare the equipment .
4 - Explain the procedure to the mother During the procedure:
5 - Clean the radiant warmer/ incubator properly before use.
6 - Switch on the main electrical supply.

## Slide 5
7 - Put the baby sheet on the bed. Arrange all necessary items near the bed.
8 - Put the radiant warmer on the manual mode with 100% heater output so that the temperature of all items likely to come in contact with the baby, are warm.
9- Once for radiant warmer is ready. Switch to skin mode with desired setting.
10 -Read temperature on display. Abdominal skin temperature should be 95.9% to 97.7 F ( 35.5o to 36.5o) .
11-Tape the probe onto the infant's abdomen b/w the umbilicus and xiphoid process in supine position and groin area in prone position.

## Slide 6
12 -Note the length of time of the radiant waves.
13- Maintain the fluid and electrolyte balance with 30% extra fluid.
14 - Place only one baby under each radiant warmer.
15-Check the temperature of the warmer and of the room every hour and adjust the temperature setting accordingly. Record the heater output in each shift (every 6 hours).
16 - Move the baby with the mother as soon as the baby no longer requires frequent procedures and treatment.

## Slide 7
After procedure:
17 – Wash hand .
18 – Put the enfant in comfortable position.
19 – Record and report any abnormality
For Disinfection:
1- For daily cleaning of front panel use damp cloth soaked in mild detergent.
2- Do not use spirit or other chemicals.
3- Bassinet, cot should be disinfected daily using soap/ detergent solution or disinfection solution

## Slide 8: Care of baby under phototherapy:
Definition:
Phototherapy is the procedure in which the baby is exposed to visible lights which causes the photo-oxidation and photo isomerization of bilirubin into water soluble, colorless form of bilirubin.

## Slide 9
Indications:
It is used when bilirubin level is:
1- 5-9 mg/dl at the 1st day of life
2- 9/15mg/dl at the 2nd day of life
3- 15/20 mg/dl at the 3rd day of life

## Slide 10
Role of nurse while giving phototherapy:
1- Check the lights of the phototherapy unit before use, no loose electric connection should be there.
2- Clean the glass surface of the phototherapy unit .
3- The lamp should be 5-8 cm over the incubator or 25-30 cm from the baby skin.
4- The eyes and the genitalia should be covered while phototherapy is in use.
5- Eye patches should be removed every 4 hourly .
6- The eye shield should not be too tight or too loose .

## Slide 11
7- Turn the position of the baby so that the entire body surface gets exposure.
8- Cleanse skin frequently to prevent irritation .
9- Monitor infant's temperature frequently.
10- Daily weight and close monitoring of I/O must be done .
11- Encourage breast feeding every 2 hourly.
12- Observe skin, mucous membranes and stool .
13- Take the baby out of the phototherapy at times (while feeding).
14- Bilirubin level should be followed for at least 24hours after discontinuing phototherapy

## Slide 12
Side effects of phototherapy:
1-Dehydration due to Increase insensible water loss .
2- GI effects such as diarrhea, increase passage of loose green stool.
3- Dark yellow urine.
4-Erythema and skin rashes.
5- Hyperthermia.
6- Irritability.
7- Bronze baby syndrome.
8- Retinal damage.
9- Cell damage and mutations.

## Slide 13
MY BEST WISHES..
THANK YOU..