## Slide 1: Measuring blood glucose level
Prepared by/
Mona Abd EL-Nasser

## Slide 2: Outlines
Definition
Purpose
Equipment
Procedure

## Slide 3: Definition
Is a method of assessing the concentration of glucose in the blood

## Slide 4
Tests are performed rapidly and easily by using a reagent strip (e.g. Glucostix)e
Site
Where a minute drop of capillary blood is obtained from the client’s digits (finger or toe) heel.

## Slide 5: Purpose:
Develop confidence in looking after the diabetic client
Immediately detect if a client’s blood sugar levels is too high (hyperglycemia) or too low (hypoglycemia)
Alert physician if the regimen is effective or not basing on the series of test results
Understand the relationship between blood glucose levels and the amount of exercise done by the client, the food intake, medications taken and lifestyle

## Slide 6
General consideration:
Before taking the device to the patient, the monitor and testing strips need to be checked for the following:
Testing strips are in date and have not been left exposed to light, heat and moisture.
The monitor and test strips have been calibrated together.
If a new pack of strips is required, the monitor is recalibrated

## Slide 7
Equipment:
Reagent strips or test strip
Clean Gloves
Alcohol pads
Lancets or lancing device
Portable glucose meter
Pen and Logbook for documentation

## Slide 8
Procedure
1-Review the patient’s medical history for diabetes type, medications, and/or anticoagulant therapy
2-Determine if the test requires special timing; for example, before or after meals.
Blood glucose monitoring is usually done prior to meals and the administration antidiabetic medications

## Slide 9
3-Gather equipment needed :Gloves, alcohol swab, lancet, gauze, reagent strips, Glucometer

## Slide 10
4-Determine if blood glucose meter needs to be calibrated.
5-Identify patient and introduce your self
6-Explain procedure to patient
7-Maintain body mechanics and privacy
8-Assess patient’s sites for skin puncture
9-Perform hand hygiene.

## Slide 11
10-Have patient wash hands with soap and warm water,
and position the patient comfortably in a semi-up right position in bed or upright in a chair.
Encourage patient to keep hands warm.
Hospital policy may require use of alcohol
swab only not water, to clean the puncture site

## Slide 12
11-Ensure that puncture site is completely dry prior to skin puncture
.
12-Remove a reagent strip from the container
and reseal the container cap. Do not touch the
test pad portion of the reagent strip

## Slide 13
13-Follow the manufacturer’s instructions to prepare the meter for measurement.
14-Place the unused reagent strip in the glucometer
15-Apply non-sterile gloves.

## Slide 14
16-Keep area to be punctured in a dependent
position. Do not milk or massage finger site.
17-Select appropriate puncture site and
perform skin puncture. Avoid fingertip pads;
use sides of finger.

## Slide 15
18-Gently squeeze above the site to produce a large droplet of blood

## Slide 16
19-Transfer the first drop of blood (or second
drop if indicated by agency policy or manufacturer’s instructions) to the reagent strip and apply following the manufacturer ’s instructions
.

## Slide 17
20-Immediately press the timer on the meter
(unless it starts automatically with insertion of reagent strip).
21-Apply pressure, or ask patient to apply pressure,

## Slide 18
22-Read the results on the unit display.

## Slide 19
23-Turn off the meter and dispose of the test
strip, gauze, and lancet in sharp container
24-Remove non-sterile gloves and place
them in the appropriate receptacle.

## Slide 20
25-Perform hand hygiene.
26-Review test results with the patient.
27-Document results according to agency policy.