## Slide 1: Measuring glucose level via urine
Prepared by:
Dr/Mona Abd EL-Nasser

## Slide 2: Definition:
Quick and simple way to check for abnormally high levels of glucose in the urine.

## Slide 3: Indication:

## Slide 4: Results of test:
The normal amount of glucose in urine is 0 to 0.8 mmol/L (millimoles per liter).
A higher measurement could be:
 Diabetes is the most common cause of elevated glucose levels.
 In some cases, a high amount of glucose in urine can be due to pregnancy.
 Elevated levels of glucose in urine may also be a result of renal glycosuria.

## Slide 5: Advantages of urine glucose monitoring:
 Urine glucose testing is easy to do: just dip the test strip in the urine and read the result at the allocated time.
 It is less painful than blood glucose monitoring , no finger pricks to collect blood.
 Urine test strips are less costly than buying a blood glucose monitor and
its test strips.

## Slide 6: Limitations of urine glucose monitoring:
 A urine glucose test does not reflect blood glucose level at the time of testing; instead, it gives an indication of blood glucose level over the past several hours.
 A urine glucose test does not give any information about low blood glucose levels, as glucose is only found in the urine when the blood glucose level is above 10 mmol/L
 The results of a urine glucose test are influenced by the volume and concentration of urine that you pass, which will vary with the amount of fluid consumed and fluid loss due to such things as heavy sweating or
vomiting.

## Slide 7
 Urine glucose tests designed for home use rely on interpreting a color change to define the result. Subtle color differences may be difficult to interpret.
 If a urine glucose test is not read at the specified time after applying the urine to the test strip, then the result is prone to error.
 Some medications may interfere with the results of urine glucose testing.

## Slide 8: Patient preparation:
 Drinking enough water
 Tell doctor about any medications or supplements that may affect the
results.
 Cleaning genital area with water before providing a sample of urine

## Slide 9: Equipment:
 Gloves
 Testing strips and comparison chart
 Cup for urine
 Protected testing area (waterproof disposable pad)
 Timing device (watch)

## Slide 10: Procedure:
Rational | Procedures steps
Having equipment prepared and available promotes organization | 1-Hand washing and gather equipment needed
To initiate therapeutic relationship | 2-Identify patient and introduce yourself.
To decrease anxiety | 3-Explain procedure to patient and toavoid contamination with stool or toilet
To decrease anxiety | 4-Maintain body mechanics and privacy
Reduces transmission of microorganisms | 5-Place non-sterile gloves.
 | 6-Place cup of urine on protected area (waterproof disposable pad)
 | 7-Dip testing strip in urine, tap off excess

## Slide 11
Because if test is not read at the specified time after applying the urine to the test strip, may result in error. | 8-Time appropriately
To rule out glucosuria or not | 9-Compares strip to comparison chart, accurately read results
Reduces transmission of microorganisms | 10-Dispose of all supplies appropriately
This reduces transmission of microorganisms. | 11-Remove and dispose of gloves and Wash hands
This promotes patient participation in care. | 12-Review test results with the patient.
 | 13-Documentation of any abnormalities