## Slide 2
Sterilization

## Slide 3
Prepared by \ Shimaa Kebary
Demonstrator at Medical Surgical Department

## Slide 4
Sterilization: -
is the complete destruction of all microorganisms, leaving form
of organisms, including spores. Sterilization can be achieved by physical,
chemical and physiochemical means. Chemicals used as sterilizing agents are
called chemisterilants.

## Slide 5
Sanitization
is the process of chemical or mechanical cleansing, applicable in
public health systems. Usually used by the food industry. It reduces microbes on
eating utensils to safe, acceptable levels for public health.

## Slide 6
Asepsis:
is the employment of techniques (such as usage of gloves, air filters,
U.V. rays etc) to achieve microbe-free environment.

## Slide 7
Antisepsis:
is the use of chemicals (antiseptics) to make skin or mucus
membranes devoid of pathogenic microorganisms.

## Slide 8
Bacteriostasis:
is a condition where the multiplication of the bacteria is
inhibited without killing them.

## Slide 9
Bactericidal:
is that chemical that can kill or inactivate bacteria. Such chemicals
may be called variously depending on the spectrum of activity, such as
bactericidal, virucidal, fungicidal, microbicidal, sporicidal, tuberculocidal or
germicidal.

## Slide 10
Antibiotics:
are substances produced by one microbe that inhibits or kills
another microbe. Often the term is used more generally to include synthetic and
semi-synthetic antimicrobial agents.

## Slide 11: Uses of Sterilization
1. Sterilization for surgical procedures: Gloves, aprons, surgical instruments,
syringes etc. are to be sterilized.
2. Sterilization in microbiological works like preparation of culture media,
reagents and equipment where a sterile condition is to be maintained

## Slide 12: Principles of Surgical Asepsis
1. All objects used in a sterile field must be
Sterile.
2.A sterile object becomes non-sterile when touched by a non-sterile object.
3. Sterile items that are below the waist level, or
items held below waist level, are considered to be non-sterile.

## Slide 13: Con ...
4. Sterile fields must always be kept in sight to
be considered sterile.
5. When opening sterile equipment and adding
supplies to a sterile field , take care to avoid
contamination.
6. Any puncture, moisture , or tear that passes through a sterile barrier must be
considered contaminated.

## Slide 14: Con..
7. Once a sterile field is set up, the border of one
inch at the edge of the sterile drape is considered non-sterile.
8. If there is any doubt about the sterility of an
object, it is considered non-sterile.

## Slide 15: Con…
9. Sterile persons or sterile objects may only contact sterile areas; non-sterile
persons or items contact only non-sterile areas.
10. Movement around and in the sterile field must not compromise or contaminate the sterile
field.

## Slide 16: Factors affecting in selecting method of sterilization
1- Nature and number of organisms.
2- Type of equipment.
3- Intended use of equipment.
4- Available method of sterilization.
5- Available time.

## Slide 17: Nursing precaution for cleaning supplies and equipment before sterilization:
1-Wear water proof gloves at time.
2-Rinse the articles first with cold running water to remove organic material.
3-Wash the articles after rinsing in warm water contains soap or detergent.

## Slide 18
4-Use brush with stiff bristles which facilitates removal of organisms.
5- Rinse and dry the articles.
6-Prepares the cleaned equipment for sterilization

## Slide 19: Classification methods of sterilization and disinfection
Physical Agents.
Chemical Agents.
Radiation.

## Slide 20: Physical Agents
1. Heat or steam(autoclaving)
2. Boiling water
3. Radiation
4. Filtration

## Slide 21
Physical Agents:
Sterilization by heat :
Heat is most effective and a rapid method of sterilization and disinfection.
Excessive heat acts by coagulation of cell proteins. Less heat interferes metabolic reactions.

## Slide 23
Sterilization occurs by heating above 100°C
which ensure lolling of bacterial spores. Sterilization by hot air in hot air oven
and sterilization by autoclaving are the two most common method used in the
laboratory.

## Slide 24: Types of Heat:
A. Sterilization by moist heat
B. Sterilization by dry heat

## Slide 25
A. Sterilization by moist heat:
Moist heat acts by denaturation and coagulation of protein, breakage of DNA
strands, and loss of functional integrity of cell membrane.

## Slide 26: (I). Sterilization at 100°C
Boiling:
Boiling at 100°C for 30 minutes is done in a water bath. Syringes , rubber goods and surgical instruments may be sterilized by this method. All bacteria and certain spores are killed. It leads to disinfection.

## Slide 27: Important points for boiling:
A- All instruments are opened before immersing them completely.
B- The time taken for boiling should commence after cold instruments have
been immersing and the water has started to boil again.

## Slide 28
2. Steaming.
Steam (100°C) is more effective than dry heat at the same
temperature as: (A) Bacteria are more susceptible to moist heat, (B) Steam has
more penetrating power, and (C) Steam has more sterilizing power as more heat
is given up during condensation.

## Slide 29
Steam Sterilizer. It works at 100°C under normal atmospheric pressure i.e.
without extra pressure. It is ideally suitable for sterilizing media which may be
damaged at a temperature higher than100°C.
It is a metallic vessel having 2 perforated diaphragms (Shelves), one above
boiling water, and the other about 4" above the floor. Water is boiled by electricity, gas or stove. Steam passes up. There is a small opening on the roof of the instrument for the escape of steam.

## Slide 32
Sterilization is done by two methods :
(A) Single Exposure for 11/2 hours. It leads to disinfection.
(B) Tyndallization (Fractional Sterilization). Heat labile media like those
containing sugar, milk, and gelatin can be sterilized by this method.

## Slide 33
Steaming at
100°C is done in steam sterilizer for 20 minutes followed by incubation at 37°C
overnight. This procedure is repeated for another 2 successive days. That is
'steaming' is done for 3 successive days. Spores, if any, germinate to vegetative
bacteria during incubation and are destroyed during steaming on second and
third day. It leads to sterilization.

## Slide 34
II. Sterilization above 100°C: Autoclaving
Autoclaving is one of the most common methods of sterilization.

## Slide 36: Principle
done by steam under pressure .Steaming at temperature higher than 100°C is used in autoclaving
The temperature of boiling depends on the surrounding atmospheric pressure.
Ahigher temperature of steaming is obtained by employing a higher pressure.

## Slide 37
121°C temperatures is obtained. This is kept for 15 minutes for sterilization to kill spores.
It works like a pressure cooker. Sterilization holding time' is the time for which the entire load in the autoclave requires to be exposed.

## Slide 38: Autoclave
is a metallic cylindrical vessel. On the lid, there are:
(1) A gauge for indicating the pressure,
(2) A safety valve, which can be set to blow off at any desired pressure,
(3) A stopcock to release the pressure. It is provided with a perforated diaphragm.

## Slide 39: Checking of Autoclave for Efficiency.
Methods:
(i) Spores of Bacillus stearothermophilus are used. Spores withstand 121°C heat
for up to 12 min. Strips containing these bacteria are included with the material
being autoclaved. Strips are cultured between 50°C and 60°C for surviving
spores. If the spores are killed the autoclave is functioning properly.
(ii)Automatic Monitoring System

## Slide 40: Factors affect the time and temperature
1- Size of Autoclave.
2- Amount of load.
3- Type of material for sterilization.

## Slide 41
Time:
143°C for minutes
121°C for 15 minutes
126°C for 10 minutes
Advantages of autoclave containers:
1- Allow steam to penetrate it to sterilize its contents.
2- Afford adequate protection against bacterial contamination
3- Be light to transport.
4- Have a long shelf life and inexpensive

## Slide 42
Types of equipment:
Paper
Metal
Cotton clothes
Linen

## Slide 43: III. Sterilization below 100°C.
1. Pasteurization. Pasteurization is heating of milk to such temperature and for
such a period of time so as to kill pathogenic bacteria that may be present in
milk without changing colour, flavour and nutritive value of the milk. Mycobacterium bovis, Salmonella species, Escherichia coli and Brucella species
may be present in milk. It does not sterilize the milk as many living organisms
including spores are not destroyed.

## Slide 44: Methods of Pasteurization:
(I) Flash Method.It is "high temperature- short time method". Heating is done
at 72°C for 15 seconds.
(II) Holding Method. Heating is done between 63°C and 66°C for 30 minutes.
2. Inspissations. Is done between 75°C to 80°C, Inspissations means stiffening of
protein without coagulation as the temperature is below coagulation
temperature. Media containing serum or egg is sterilized by heating for 3
successive days. It is done in 'Serum Inspissator'.

## Slide 45: B. Sterilization by Dry Heat
Mechanisms. (1) Protein denaturation, (2) Oxidative damage, (3) Toxic effect of
elevated electrolyte (in absence of water).Dry heat at 160°C (holding
temperature for one hour is required to kill the most resistant spores). The
articles remain dry. It is unsuitable for clothing which may be spoiled.

## Slide 46
1. Red Heat. Wire loops used in microbiology laboratory are sterilized by
heating to 'red' in Bunsen burner or spirit lamp flame. Temperature is above
100°C. It leads to sterilization.
2. Flaming. The article is passed through flame without allowing it to become
red hot, e.g. scalpel. Temperature is not high to cause sterilization.
3. Sterilization by Hot AirOven.

## Slide 47
Sterilization by Hot Air Oven.
Hot Air Oven (Sterilizer). It is one of the most common methods used for
sterilization. Glass wares, swab sticks, all-glass syringes, powder and oily
substances are sterilized in hot air oven. For sterilization, a temperature of
160°C is maintained (holding) for one hour. Spores are killed at this
temperature. It leads to sterilization.

## Slide 49
Hot Air Oven is an apparatus with double metallic walls and a door. There is an
air space between these walls. The apparatus is heated by electricity or gas at the bottom. On heating, the air at the bottom becomes hot and passes between the
two walls from below upwards, and then passes in the inner chamber through
the holes on me top of the apparatus. A thermostat is fitted to maintain a
constant temperature of 160°.

## Slide 50: Uses
Metal item.
Glassware and all glass syringes.
Powders.
Metal cannel such as lumbar puncture needless and some of ophthalmic
instruments but insufficient to destroy all microorganisms

## Slide 51: 2-Chemical solutions.
In practice, certain methods are placed under sterilization which in fact do not
fulfill the definition of sterilization such as boiling for 1/2 hr and pasteurization
which will not kill spores.

## Slide 52
1-Ethylene oxide gas:
they destroy microorganisms and spores by
interfering with metabolic process in cell. But they are toxic to humans.
Used for sterilization of sensitive equipment such as endoscopes when
combined with a chemical vapor.

## Slide 53
Disadvantages of gas:
It has a pungent smell.
It is irritant to eye, skin and mucous membranes.
It has poor properties of penetration and diffusion into fabrics or narrow tubes such as catheter.

## Slide 54
2-Chemical solutions:
Used for instrument and equipment disinfections and for
Housekeeping disinfections (Chlorines, butadiene, and alcohol). But does not
destroy all spores and may cause corrosion on metal surfaces.

## Slide 55: Nursing precaution used for chemical solutions
Never use chemical if more reliable methods are available.
Cleanaing is the first and most important step in disinfections.
Total surface contact is essential.
Equipment has to be rinsed after immersion in chemical solution by sterile water.
Antiseptics may themselves become contaminated by incorrect use.

## Slide 56: 3-Radiation
Used for food, plastic and other sensitive items, object must be directly
exposed to ultraviolet radiation on all surfaces but poses risk to personnel.
(Gamma rays). Large dose of radiation is required to kill small virus.